## Slide 1
Introduction to Vehicular Ad Hoc Networks Simulation (Veins) in OMNeT++
Jaehoon (Paul) Jeong
Department of Computer Science and Engineering
pauljeong@skku.edu

## Slide 2: Recommended Installation Environment
OS | Ubuntu Linux 16.04
OMNeT++ | Version 5.4.1
SUMO | Version 0.32.0
Veins | Version 4.7.1
INET Framework | Version 4.0.0

## Slide 3
SUMO Installation
Version: 0.32.0

## Slide 4: Required Tools Installations
$ sudo apt-get install autoconf
$ sudo apt-get install libproj-dev proj-bin proj-data libtool libgdal1-dev libxerces-c3-dev libfox-1.6-0 libfox-1.6-dev python-dev python3-dev

## Slide 5: Configure & Make SUMO
Download SUMO source from https://sourceforge.net/projects/sumo/files/sumo/version%200.32.0/sumo-src-0.32.0.tar.gz/download
Go to sumo-0.32.0 folder
$ ./configure --prefix the path of the installation folder
(e.g., /home/iotlab/usr/sumo-0.32.0/bin)
$ make
(in case of multicore (e.g., 4), for speeding compiling, use: make -j 4)
sudo make install
When the make is finished, run ./bin/sumo, it should show version information:

## Slide 6: Check Installed SUMO Version

## Slide 7
Import Veins Project

## Slide 8: Downloading Veins & Inet
Download Veins and inet HW4 from iCampus
Change the mode by command “chmod –R 777 {veins and inet directory name}”
  Ex)
Open a new terminal, type omnetpp to start OMNeT++ IDE

## Slide 9: Importing Veins & Inet (1/2)
2) Import Veins
Click File -> Import -> Existing Projects into Workspace ->Next -> Browse -> Choose the folder of veins -> Finished

## Slide 10: Importing Veins & Inet (2/2)
Select root directory of your Veins project, and then click Finish.
That is the same way, import inet or other OMNeT++ projects to the workspace.

## Slide 11: Running SUMO
3) Run the sumo launched file in veins directory
To connect to SUMO when you run Veins in OMNeT++.
$ ./sumo-launchd.py -v -c /home/chris/usr/sumo-0.32.0/bin/sumo-gui

## Slide 12: Launch veins
4) Run Veins
In Project Explorer, right-click Veins project, and choose Build Project. It may take several minutes.
In Project Explorer, find veins -> examples -> veins -> omnetppTestRouting.ini, and then right click it -> Choose Run As -> OMNeT++ Simulation. It may take several minutes.

## Slide 13: How Veins Works?
OMNeT++: Network Simulation
SUMO: road traffic can be modeled and complex interactions between both domains examined.
TraCI: The protocol for this communication between OMNeT++ and SUMO
Notes: TraCI: Traffic Control Interface

## Slide 14: Example of a Running Veins Simulation
Click the Run button to run the program, and then you will see Sumo gui window.
(For test, we reduce the number of cars.)

## Slide 15
Basic SUMO useful tools

## Slide 16: NETGENERATE
Tool: generate map
  https://sumo.dlr.de/docs/NETGENERATE.html
  Usage
    netgenerate --help
  Example
netgenerate -g --grid.x-number 5 --grid.y-number 7 --tls.guess -L 3 -S 20
netgenerate -c <CONFIGURATION> create net from given configuration netgenerate --grid [grid-network options] -o <OUTPUTFILE> create grid net netgenerate --spider [spider-network options] -o <OUTPUTFILE> create spider net netgenerate --rand [random-network options] -o <OUTPUTFILE> create random net
Notes: NETGENERATE generates abstract road networks that may be used by other SUMO-applications.

## Slide 17: Real Map
OpenStreetMap
  https://www.openstreetmap.org/
  Usage
    netgenerate --help
  Example
Java OpenStreetMap Editor(JOSM): https://josm.openstreetmap.de/

## Slide 18: NETCONVERT
Tool for road networks import and conversion
  https://sumo.dlr.de/docs/NETCONVERT.html
  Usage
    netconvert --help
  Example
netconvert --osm-files ./*.osm --remove-edges.by-vclass hov,taxi,bus,delivery,truck,tram,rail_urban,rail,rail_electric,motorcycle,bicycle,pedestrian -o *.net.xml
netconvert -s *.net.xml --tls.guess
Notes: NETCONVERT imports digital road networks from different sources and generates road networks that can be used by other tools from the package.

## Slide 19: Run Vehicle in the road network
Tool-generated map
  Generating random traffic in road network:
    in your sumo installation folder: /sumo-0.21.0/tools/
    Ref: https://sumo.dlr.de/docs/Tools/Trip.html I
    ./randomTrips.py
  Usage
    randomTrips.py --help

## Slide 20
Introduction to Veins Implementation Structure

## Slide 21: Veins nodes
Vehicles
  Used to Simulate cars
Road-Side Unit (RSU)
  Deployed in Road Network as infrastructure
Scenario
  In modules, we mainly have application, mac, messages, nic, obstacle, mobility and phy subdirectories.

## Slide 22: Submodules
Vehicles
  Used to Simulate cars
Road-Side Unit (RSU)
  Deployed in Road Network as infrastructure
Scenario
  In modules, we mainly have application, mac, messages, nic, obstacle, mobility and phy subdirectories.

## Slide 23: Veins Running View

## Slide 24: References
SUMO installation:
  https://sumo.dlr.de/docs/Installing/Linux_Build.html
SUMO tools:
  https://sumo.dlr.de/docs/SUMO_User_Documentation.html#additional_tools
Veins Documentation
  https://veins.car2x.org/

## Slide 25: Thanks!